## Slide 1
VIRTUAL REALITY
WELDING TRAINING
CODED WELDER: OFO 651202-02
KM-04: SMAW/MMA PROCESS, NQF LEVEL 3, CREDITS 2

## Slide 2: ABOUT THIS MODULE
The focus of the learning in this knowledge module is to build an understanding of the SMAW welding process as applied in the welding trade.
The learning will enable learners to demonstrate an understanding of:
KM-04-KT01: SMAW general health, safety and environmental protection concepts (20%)
KM-04-KT02: SMAW welding equipment and typical parameters (50%)

## Slide 3: KM-04-KT01: SMAW general health, safety and environmental protection concepts.
A recap from KM – 01, lets discuss the welding PPE.

## Slide 4: Other Safety Equipment and Protective Gear for Welding.
Welding requires various safety gear, including ear protection, respirators for air filtration, helmets with tinted lenses, leather clothing, gloves, and steel-toed boots.
Auto-darkening helmets are a convenient choice.
Always follow safety rules and equipment recommendations for welding machines.

## Slide 5: Key Safety Equipment and Protective Gear for Welding
Ear Protection
Respirator
Helmets and Hand-shields
Auto-Darkening Helmets
Outer Clothing, Gloves, and Shoes
Full-Length Leather Apron and Shoulder-and-Sleeve Garment
SMAW Safety Rules
Caution: Always use proper eye protection with the right shade of darkness, and those who wear glasses can get special magnification lenses. Replace clouded outer lenses promptly.

## Slide 6: Welding Machine and Personal Safety
Welding Machine Safety Essentials
Follow manufacturer's guidelines.
Welding Personal Safety:
Wear proper eye and body protection.
Ensure adequate ventilation.
Keep work areas clean and organized.
Be aware of fire safety measures.
Understand procedures thoroughly.
Avoid working near hazards.
Maintain focus and avoid distractions.
Keep equipment in good condition.
- Welding Procedural Safety:
Understand procedures before starting.
Eye protection is crucial.
Wear safety clothing.
Maintain good ventilation.
Use safety glasses with side shields.
Keep a safe distance from hazards.
Secure weldments and inspect equipment.
Maintain a clean workspace.
Use a fire extinguisher if needed.
Stay focused and avoid horseplay.
Attend to injuries promptly.

## Slide 7: Electric shock, harmful fumes and gases
Undertaking welding activities can expose welders to invisible gaseous fumes, including ozone, nitrogen oxides, chromium and nickel oxides, and carbon monoxide which can easily penetrate their lungs.
Depending on the gas or fume, the concentration, and duration of your exposure, the resultant damage can be severe.

## Slide 8: Welding Hazards (prevention and solutions recap)
Fire Risk: Sparks and molten metal can ignite flammable materials.
Fire Extinguishers: Properly maintain and know the location of fire extinguishers.
Fuel Gases and Oxygen: Handle with care; store away from heat, flames, and sparks.
Gas Leaks: Check pressurized gas equipment for leaks before use.
Electric Shock: Proper grounding, equipment maintenance, and avoiding wet areas are essential.

## Slide 9
Welding Hazards (prevention and solutions recap) p2
Toxic Fumes: Weld in well-ventilated areas to prevent exposure to smoke, dust, and toxic fumes.
Welding Closed Containers: Follow safety steps to avoid explosions when welding closed containers.
Welding in Confined Areas: Ventilate and monitor gas levels; avoid working alone.
Personal Injuries: Burns are common, so wear protective clothing and mark hot objects.
Radiation: Welding produces harmful visible and invisible light; protect eyes and skin.
Arc Flash Burn: Exposure to welding arc flash can lead to eye and skin injuries.

## Slide 10: Assessment activity
State FIVE precautionary measures you would take with respect personal safety when welding.
Briefly describe FIVE safety precautions when using a welding machine? All answers must refer to the welding machine.
List Eight items of PPE typically used by welders.

## Slide 11: KT02: SMAW Welding Equipment and Typical Parameters
- SMAW welding process
Manual Metal Arc welding (MMA) is often referred to as referred to as Shielded Metal Arc Welding (SMAW) or stick welding.
It uses electrode rods consisting of a wire core with an external coating (flux) containing mixtures of substances such as chemicals, minerals and iron powder.
An arc is created between the electrode and the workpiece, melting the coating to form a protective slag.
The resulting weld metal is used for both joining and surfacing metal products and after welding, the slag layer on the weld joint must be removed.
MMA welding can be mechanized through gravity arc welding, securing the electrode feeder frame, allowing a single welder to manage 3-5 arcs simultaneously.

## Slide 12: Components of a SMAW welding system
A workpiece lead.
An electrode holder
A power source of adequate current rating and duty cycle
A SMAW electrode compatible with the output of the power source
A suitably sized welding cable

## Slide 13: MMA welding can be performed using either DFC or AC, which means that many types of power sources can be used.
Advantages of using AC
Relatively simple equipment.
Can be used within different environments including outdoors, in fabrication shops,
Disadvantages of using AC
Most portable of all welding processes.
No need for separate gas shielding.
on pipelines and refineries, on ships and bridges, and more.
Is not sensitive to wind and draft.
AC welding limits electrode choices.
A high open-circuit voltage (at least 50V) is necessary for power sources.
Stick welding is slower than other methods.
It's a complex process requiring skilled welders.
Removing slag post-welding is time-consuming.
Thinner metals can be challenging to weld.
Frequent replacement of welding rods is needed.
Stick welding may lead to excessive spatter, rough surfaces, and porosity.

## Slide 14: Assessment Activity
Give FIVE reasons why welding in a closed container is so dangerous to the welder?
Briefly describe how you will ensure safe welding inside a closed container by listing FOUR steps to avoid danger.
Give FIVE steps you would take to reduce the risk of danger when welding in a confined space.

## Slide 15: SMAW equipment
The key equipment used in Shielded Metal Arc Welding consists of:
The Power Source
The Welding Cables
The Electrode Holder
The Covered Electrodes

## Slide 16: The Power Source
The Power Source is the welding machine. Several different types of power sources are available and can be either:
Alternating current (AC) machines,
Direct current (DC) machines, or
A combination of both.

## Slide 17: Key points on the SMAW equipment
Welding machines can be electrically, or petrol/diesel driven for areas without electricity.
MMA welding creates an electric arc between the electrode and base metal, melting both.
The power source for MMA welding has current and voltage adjustment knobs and may include voltmeters and ammeters.
Three types of welding machines are typically used for SMAW: AC, DC, and rectifier.
AC welding machines are versatile, simple, and low-maintenance, suitable for outdoor use.

## Slide 18
DC welding machines offer a wider range of electrode choices, adjustable polarity, and can weld thinner materials and non-ferrous metals.
Rectifier welding machines combine advantages of AC and DC and are used with Tig and Mig welding.
Welding cables consist of copper wire strands covered in insulation material.
The electrode holder securely holds the welding electrode.
Electrodes are coated wires that provide shielding, arc stability, and slag formation during welding.

## Slide 19
Electrodes vary in type, size, and composition, with cellulose, rutile, and basic types being common.
Cellulose electrodes offer excellent penetration due to high hydrogen content.
Acid electrodes contain iron and manganese oxides, and iron powder can enhance efficiency.
Penetration electrodes use a mixed rutile/acid coating with cellulose for increased arc penetration in horizontal welding of I-joints.

## Slide 20: Assessment Activity
Briefly describe the SMAW welding process in TEN clear steps.
Make a simple line sketch of a basic SMAW welding system – listing the FIVE important parts.
State the THREE types of SMAW welding machines.
List the FIVE most important welding parameters for SMAW welding

## Slide 21: SMAW process applications and limitations
The welding equipment is can be considered straightforward to use. The equipment is:
  Particularly suitable for jobs such as the erection of structures.
  It can also be used outdoors, as opposed to other methods requiring shielding gas, which is unsuitable in windy conditions.
However, its arc time factor is relatively low, due to the need to remove slag after the welding task and the change-over of electrodes.

## Slide 22: Recap on the Critical Welding Variables (CLASS):
Current Setting
Arc Length
Electrode Angle
Travel Speed
Electrode Selection

## Slide 23: KT03 SMAW COVERED ELECTRODES
Types of SMAW process electrodes
The metal composition of the electrode is similar to the parent metal, it consist of a wire rod with a flux coating.
One end of the electrode rod is uncoated and clamped in the electrode holder.
The rod melts in the welding arc, forming the filler metal for the weld.
The flux coating burns to create a shielding gas and slag coating on the weld.

## Slide 24
Damaged or damp electrodes should not be used to avoid weld defects.
Electrodes come in various sizes and metals to match different welding needs and different types are marked with numbers or color codes.
Welders need to understand and select electrodes based on the size, metal type, joint, and other welding requirements.
Proper electrode placement in the holder is at an angle of approximately 45 degrees.

## Slide 25: Function of flux covering in mild steel electrodes
Stick electrodes consist of a metal rod surrounded by a coating called flux.
The flux coating determines where and how an electrode can be used.
When an arc is struck, the flux undergoes complex chemical reactions.
Flux ingredients burn in the welding arc, releasing shielding gas.
The shielding gas protects the molten weld pool from atmospheric impurities.
As the weld pool cools, the flux creates slag to prevent oxidation and weld porosity.

## Slide 26: Flux coating and the gas shield

## Slide 27: Composition of mild steel Electrode fluxes
Flux coating on welding rods serves multiple functions.
It protects the weld pool and solid metal from atmospheric contamination.
Flux helps remove impurities from the weld pool.
It contains ionizing elements for arc stability, especially with AC power sources.
Alloys in flux contribute to weld ductility and tensile strength.
Flux may include a higher concentration of iron powder for increased deposition rates.
Added deoxidizers in flux act as cleaning agents and can penetrate corroded or dirty workpieces.

## Slide 28
The End